## Slide 1
NORTHWOOD FOUR CORNERS CIVIC ASSOCIATION
June 12, 2025
University Boulevard Corridor Plan

## Slide 2: UNIVERSITY BOULEVARD CORRIDOR PLAN (UBCP)
PLAN VISION
  Pedestrian-oriented
  Multimodal
  Safe, accessible, and healthy travel options
  Vibrant, connected communities
  Diverse range of housing options
  Supported by Bus Rapid Transit (BRT)

## Slide 3: PLAN FRAMEWORK
FOUR DISTRICTS in UBCP
3 Future BRT Stops
NFCCA focus:
  Arcola Ave District
  Dennis Ave District
  Four Corners District

## Slide 4
Urban Design Strategy
Promote transit-supportive development near BRT
Expand housing choice on properties fronting University Blvd. between planned BRT stops
Identify multimodal improvements
Environmental Sustainability
Recommend developing University Blvd. as “Cool Corridor”
Tree canopy, shaded transit shelters
Runoff reduction landscaping
Design for trees, reduce utility line conflicts
Increase tree canopy and landscaping
Promote energy conservation options for redevelopment

## Slide 5: Transportation
Complete network of comfortable sideways and bikeways connected by safe protected crossings
Support opportunities for micro-mobility, bike share and electric charging stations

## Slide 6
Transportation -- University Boulevard
10’ buffered sidepaths on both sides of University Blvd.
Dedicated transit lanes along University Blvd. and Colesville Rd.
Network of streets along University Blvd. with redevelopment
With redevelopment or BRT implementation consolidate, remove, or relocate driveways on University Blvd.

## Slide 7
Transportation – Caddington Avenue

## Slide 8
Transportation – Four Corners
Lorain to Colesville Rd. – East & West

## Slide 9
Transportation Four Corners

## Slide 10: Transportation – Four Corners
In near-term maintain existing couplet
Repurpose one lane in each direction for buffer and wider sidewalk or sidepath
Study additional street connections to achieve long-term vision for more connected network and regular street pattern
Study options for improving transit performance, multimodal safety, human scale, and street buffers over traffic capacity and travel speed

## Slide 11
Transportation Four Corners—BRT Station

## Slide 12
Transportation Four Corners—BRT Station

## Slide 14
Floor Area Ratio (FAR)
FAR limits:
Maximum square footage of building compared to lot size
Mix of uses for residential or commercial/retail
Example: Lot with 10,000 square feet
FAR of CRT 2.25, C-1.5, R-2.0, Height 60
Maximum building size is 22,500 square feet
Developer decides ratio of commercial vs residential
  15000 sq.ft. commercial & 7500 sq.ft. residential
  2250 sq.ft. commercial & 20000 sq.ft. residential
  5000 sq.ft. commercial & 17500 sq.ft. residential
Residential
Commercial
Residential

## Slide 15
Arcola Avenue
BRT District
Homes on University Boulevard and
Whittington Terrace (NFC) or
Breezewood (SFC)
Maximum Building FAR is 1.0 times lot size
Residential only.
Height 50’
Commercial Residential Town
Religious Institution Properties
(Luther Rice, Shomrai Emunah)
Maximum Building FAR is 1.5 times lot size
Commercial FAR is .25
Residential FAR is 1.5
Height 60’
Commercial Residential Neighborhood

## Slide 16
Dennis Avenue
BRT District
Commercial Residential Neighborhood
Maximum building FAR is 1 x lot size
Residential only
Four Corners BRT District
Commercial Residential Town
The Oaks
Maximum FAR 1.5
Commercial 0.25
Residential 1.5
Height 70’
Height 50’

## Slide 17
Dennis Avenue
BRT District
Commercial Residential Town
Collins Funeral Home
Homes on University
Office Buildings
Masonic Lodge
Maximum Building FAR is 1.5 x lot size
Commercial FAR 0.25
Residential FAR 1.5
Red = Build to Line
University Blvd & Dennis Avenue
intersection
Height 60’
DDennis Avenue
N

## Slide 19
Four Corners District BRT Station
Red = Build to Line
University Blvd & Colesville intersection
BRT
STOP
FLASH Bus Stations in Median Lane at Intersection

## Slide 20
Four Corners District BRT Station
Timberwood Ave homes
Homes in block on Colesville & Sutherland
Maximum building FAR is 1 x lot size
Residential only
Height 50’
Insurance Co on Sutherland
Maximum Building FAR is 1.25 x lot size Commercial FAR .05
Residential FAR 1.0
Height 40’
2
1
1
Commercial Residential Neighborhood

## Slide 21
Four Corners District BRT Station
Commercial Residential Town
Dunkin Donuts and Vacant Offices (Lorain)
Maximum Building FAR is 3.0 x lot size
Commercial FAR is 2 and Residential FAR is 1.5
Vet and Various retail/office on Univ Blvd
Maximum Building Far is 1.5 x lot size
Commercial FAR is 1.5 and Residential FAR is 1.5
Four Corners Pub/Red Maple/Pizza Hut/shops (Sutherland and Colesville)
Maximum Building FAR is 2.5 x lot size
Commercial FAR is 1.5 and Residential FAR is 2.0
Utility building/Shell gas station (Timberwood)
Maximum Building FAR is 2.0 x lot size
Commercial FAR is 1.5 and Residential FAR is 1.5
Citgo gas station (Univ. Blvd & Sutherland)
Maximum Building Far is 2.25 x lot size
Commercial FAR is 1.5 and Residential FAR is 2.0
1
4
Height 75 ‘
Height 100 ‘
2
3
5

## Slide 22
Four Corners District BRT Station
Commercial Residential Town
Median block with Papa Johns, McDonalds, 7-11, Vitamin Shop
FAR max 2.5 x lot size
Commercial FAR 1.5
Residential FAR 1.5
Post Office/Gas Stations
Max Building FAR is 2.25 x lot
Commercial FAR is 1.5
Residential FAR is 1.5
Safeway
FAR max 3.0 x lot size
Commercial FAR 1.5
Residential FAR 2.5
60 ‘ high
1
3
2
Height 100 ‘
Height 75‘

## Slide 23
Commercial Residential Town
Four Corners District BRT Station
Woodmoor Shopping Center
FAR max 3 x lot size
Commercial FAR 1.5
Residential FAR 2.5
Ethiopian Church
FAR max 1.5 x lot size
Commercial FAR 0.75
Residential FAR 1.5
Height 100 ‘